## Slide 1
Week 8 update
Jetson harness, literature policies on real hardware, and the CityFlow dispatcher result
Advisors: Prof. Gayathri Ananthanarayanan (IIT Dharwad), Dr. Marcello Traiola (INRIA)
Affan Pathan | October 2026

## Slide 2
OVERVIEW
This week in one slide
Two tasks from meet 7: fix the CityFlow routing, and run existing scheduling approaches on a real Jetson AGX Xavier
Task | What was done | Outcome
1. CityFlow dispatcher | Tried to build a dispatcher for the CityFlow dataset: relabelled frames, fine-tuned the models, searched for dispatchers with NSGA-II | Failed. Fine-tuning did not help, and the dispatchers that came out performed worse than static allocation. Put on hold
2. Scheduling policies on the Jetson | Built a real-time test harness, then implemented Clockwork, Symphony and an EdgeServing-inspired greedy policy and tested them on the Jetson AGX Xavier (682 runs: 3 deadlines, 8 traffic mixes, 4 loads, 2 to 3 seeds) | Clockwork leads goodput at tight deadlines; Symphony spends the least total energy (up to 19% less at loose deadlines); no policy has both
Takeaway. The EdgeServing-inspired policy is not EdgeServing itself: removing the paper's exit-layer knob changes the policy fundamentally, so I do not name it after the paper. Seed 2 is still running for the later mixes (two seeds there).

## Slide 3
PART 1 | HARNESS
How the harness works
Everything is fixed except the policy: the same arrivals, models and board for every policy
1. Arrivals
Random requests at a set rate (req/s), split across the four models by a traffic mix; same seed, same list
2. Four queues
One waiting line per model: yolov8 n, s, m, l
3. Policy
Whenever the GPU is free, picks which queue to serve and how many requests to batch, or waits
4. GPU
Runs that batch: copy, detect, post-process. One batch at a time
5. Results
Latency, deadline hits, drops, energy per request
Power meter
Board power read about 8 times a second, summed over the run
When the batch finishes, the policy decides again.
Held fixed
Board: Jetson AGX Xavier, 15 W mode, clocks locked
Models: YOLOv8 n, s, m, l (FP16), all loaded in memory
Each run: 15 s warm-up, 120 s measured, then drain
Deadline: one value per run (150, 600 or 2400 ms)
Takeaway. Only box 3 changes between experiments, so any difference in the results comes from the policy.

## Slide 4
PART 1 | HARNESS
How arrivals are modelled
Random requests at a fixed average rate, split across the four models by a traffic mix
Chart: traffic mix (capacity in req/s)
| l85 (13.3) | l55 (16.7) | balanced (22.4) | n40 (25.8) | skewed (27.5) | n55 (30.3) | n70 (36.8) | n85 (46.9)
yolov8n | 5 | 15 | 25 | 40 | 52.8 | 55 | 70 | 85
yolov8s | 5 | 15 | 25 | 20 | 14.9 | 15 | 10 | 5
yolov8m | 5 | 15 | 25 | 20 | 8.3 | 15 | 10 | 5
yolov8l | 85 | 55 | 25 | 20 | 24 | 15 | 10 | 5
Step | How it works
Rate | Total load Λ in req/s (8, 16, 24 or 36); queue i gets rate Λ × its share in the mix
Timing | Poisson process per queue: gaps between requests are exponential with mean 1 / rate
Input | Each request picks a random image from a fixed pool of sample images
Deadline | Arrival time plus the run's deadline (150, 600 or 2400 ms)
Seed | Fixed seed gives the identical request list for every policy, so policies see the same traffic
Takeaway. Capacity is the rate the board could serve if every batch were full (size 16); it falls as the mix leans toward the heavy model, so 16 req/s is well under capacity on n85 and above it on l85.

## Slide 5
PART 1 | HARNESS
Batch time is linear in b: batching saves the fixed term only
Measured on the board before the runs: median time of 100 batches per model and size (after 20 warm-up batches), copy + detect + post-process; line fit a + c·b
Chart: batch size b
| 1 | 2 | 3 | 4 | 6 | 8 | 12 | 16
yolov8n | 21.9 | 38.9 | 54.8 | 69.6 | 100 | 128.8 | 188.3 | 248
yolov8s | 36 | 66.2 | 91.8 | 115.2 | 167.6 | 218.4 | 318.7 | 420.1
yolov8m | 71.7 | 128 | 179.2 | 229.2 | 339 | 446.4 | 655.1 | 863.8
yolov8l | 109.9 | 197.3 | 278 | 353.6 | 514 | 675.4 | 1010.8 | 1323.2
Model | a + c·b (ms) | ms/frame, b=1 | ms/frame, b=16 | saving
yolov8n | 9 + 15·b | 21.9 | 15.5 | -29%
yolov8s | 14 + 25.4·b | 36 | 26.3 | -27%
yolov8m | 20.8 + 52.8·b | 71.7 | 54 | -25%
yolov8l | 31.8 + 80.9·b | 109.9 | 82.7 | -25%
Capacity at b up to 16: 22.4 req/s for the balanced mix, 27.5 req/s for the skewed mix. Sizes between the measured ones (5, 7, 9...) were not measured; they run slower than this fit.
Takeaway. Batching removes 25 to 29% of the per-frame time and no more, so the headroom for batching on this board is smaller than a size-independent-cost model predicts.

## Slide 6
PART 1 | HARNESS
Energy against batch size: per batch and per frame
Board energy while a batch runs, estimated from the 682 runs (not a direct calibration measurement)
Chart: Energy per batch
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
yolov8n | 0.216 | 0.371 | 0.526 | 0.681 | 0.836 | 0.991 | 1.146 | 1.301 | 1.456 | 1.611 | 1.766 | 1.921 | 2.076 | 2.231 | 2.386 | 2.541
yolov8s | 0.367 | 0.638 | 0.91 | 1.182 | 1.453 | 1.725 | 1.996 | 2.268 | 2.54 | 2.811 | 3.083 | 3.354 | 3.626 | 3.898 | 4.169 | 4.441
yolov8m | 0.785 | 1.428 | 2.071 | 2.714 | 3.357 | 4.001 | 4.644 | 5.287 | 5.93 | 6.573 | 7.217 | 7.86 | 8.503 | 9.146 | 9.789 | 10.433
yolov8l | 1.266 | 2.316 | 3.366 | 4.416 | 5.466 | 6.516 | 7.566 | 8.616 | 9.666 | 10.716 | 11.766 | 12.816 | 13.866 | 14.916 | 15.966 | 17.016
Chart: Energy per frame
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
yolov8n | 216 | 186 | 175 | 170 | 167 | 165 | 164 | 163 | 162 | 161 | 161 | 160 | 160 | 159 | 159 | 159
yolov8s | 367 | 319 | 303 | 295 | 291 | 287 | 285 | 284 | 282 | 281 | 280 | 280 | 279 | 278 | 278 | 278
yolov8m | 785 | 714 | 690 | 679 | 671 | 667 | 663 | 661 | 659 | 657 | 656 | 655 | 654 | 653 | 653 | 652
yolov8l | 1266 | 1158 | 1122 | 1104 | 1093 | 1086 | 1081 | 1077 | 1074 | 1072 | 1070 | 1068 | 1067 | 1065 | 1064 | 1064
Method: whole-run board energy (power log) is fitted against the number of batches and frames of each model in the batch log. Each batch costs a fixed part (the launch time a at one shared power) plus a per-frame part. Board power is the total without the 5 V system rail; the board's own idle draw (about 4 W) is not counted in the batch.
Takeaway. Energy per frame falls 27% (n), 24% (s), 17% (m) and 16% (l) from b = 1 to 16, no larger than the time saved (29 to 25%), and most of it comes by b = 8.

## Slide 7
PART 2 | POLICIES
Three policies on one GPU: two from the literature, one inspired by it
Read from the papers: EdgeServing (arXiv 2605.05527), Clockwork (OSDI 2020), Symphony (arXiv 2308.07470)
Policy | Core idea | Waits? | Drops? | What I changed
Greedy-2D (EdgeServing-inspired) | Picks queue and batch size by an urgency score summed over every queued job | no | no | Paper picks model, exit layer and depth; the exit knob is removed, leaving (queue, batch size). Not EdgeServing itself
Clockwork | Earliest latest-start first; largest batch the oldest deadline allows; cancels hopeless requests | no | yes | INFER only; static p99 service times; batch sizes 1, 2, 4, 8, 16; no load/unload
Symphony | Holds each queue until the last moment to grow the batch; serves the smallest latest-start | yes, on purpose | yes | One GPU, four queues; calibrated batch sizes only; static p99 service times
Every policy gets the same deadline (150, 600 or 2400 ms per run). A miss is a request served late or dropped; goodput is the share served within the deadline. Drops are counted, never hidden.
Takeaway. The mechanisms are kept. What is dropped (exit and depth knobs, load/unload, multi-GPU staggering) does not exist with all models resident on one GPU, but it changes how the Greedy-2D and Symphony policies behave.

## Slide 8
RESULTS | GOODPUT
Goodput: the share of requests that meet their deadline
Goodput = requests completed within the deadline / all requests that arrived in the window; dropped requests count as misses
Traffic mix | Share of requests (n / s / m / l) | Capacity (req/s) | Low load: 8 req/s | Medium load: 16 req/s | High load: 24 req/s
heavy mix (l55) | 15 / 15 / 15 / 55 % | 16.7 | 48% of capacity | 96% | 144%
balanced mix | 25 / 25 / 25 / 25 % | 22.4 | 36% | 71% | 107%
skewed mix | 52.8 / 14.9 / 8.3 / 24.0 % | 27.5 | 29% | 58% | 87%
light mix (n70) | 70 / 10 / 10 / 10 % | 36.8 | 22% | 43% | 65%
Each of the next slides fixes the load and shows the four mixes; inside each chart the x-axis is the deadline (150, 600, 2400 ms) and the bars are the three policies. Capacity is the rate the board sustains with full batches of 16. Values are means over the seeds run so far (3 for balanced and skewed, 2 for the heavy and light mixes; seed 2 is still running).
Takeaway. The same three loads span a mix at 22% of capacity to the same mix beyond it, so the comparison covers light, near-capacity and overloaded conditions.

## Slide 9
RESULTS | GOODPUT
Goodput at low load (8 req/s)
Goodput (%) against deadline, four mixes; 8 req/s is 48%, 36%, 29% and 22% of capacity
Chart: Heavy mix (l55): capacity 16.7 req/s, load 48%
| 150 ms | 600 ms | 2400 ms
Clockwork | 78.7 | 99.6 | 100
Greedy-2D | 59.5 | 99.7 | 100
Symphony | 71.3 | 86.7 | 94
Chart: Balanced mix: capacity 22.4 req/s, load 36%
| 150 ms | 600 ms | 2400 ms
Clockwork | 89.7 | 100 | 100
Greedy-2D | 84.5 | 100 | 100
Symphony | 78.6 | 89.6 | 96.7
Chart: Skewed mix: capacity 27.5 req/s, load 29%
| 150 ms | 600 ms | 2400 ms
Clockwork | 93.5 | 100 | 100
Greedy-2D | 91.5 | 100 | 100
Symphony | 82.1 | 91.6 | 97.9
Chart: Light mix (n70): capacity 36.8 req/s, load 22%
| 150 ms | 600 ms | 2400 ms
Clockwork | 97.3 | 100 | 100
Greedy-2D | 97.6 | 100 | 100
Symphony | 88 | 95 | 98.7
Takeaway. From 600 ms every policy meets nearly all deadlines. At 150 ms Clockwork is best or tied (79 to 97%). Symphony loses 1 to 6 points even at 2400 ms because it waits to build batches.

## Slide 10
RESULTS | GOODPUT
Goodput at medium load (16 req/s)
Goodput (%) against deadline, four mixes; 16 req/s is 96%, 71%, 58% and 43% of capacity
Chart: Heavy mix (l55): capacity 16.7 req/s, load 96%
| 150 ms | 600 ms | 2400 ms
Clockwork | 60.9 | 76.1 | 90.4
Greedy-2D | 10.4 | 11.6 | 9.7
Symphony | 52.5 | 67.3 | 82.6
Chart: Balanced mix: capacity 22.4 req/s, load 71%
| 150 ms | 600 ms | 2400 ms
Clockwork | 76.4 | 96.3 | 100
Greedy-2D | 10.8 | 60.3 | 100
Symphony | 64.4 | 80.7 | 94.8
Chart: Skewed mix: capacity 27.5 req/s, load 58%
| 150 ms | 600 ms | 2400 ms
Clockwork | 84.5 | 99.3 | 100
Greedy-2D | 62.8 | 98.9 | 100
Symphony | 70.9 | 87.9 | 97.2
Chart: Light mix (n70): capacity 36.8 req/s, load 43%
| 150 ms | 600 ms | 2400 ms
Clockwork | 93.5 | 100 | 100
Greedy-2D | 89.2 | 99.9 | 100
Symphony | 81.6 | 93.7 | 98.9
Takeaway. Clockwork has the best goodput at 150 ms on every mix. Greedy-2D collapses to about 10% on the heavy and balanced mixes at 150 ms (and on l55 at every deadline) and to 63% on skewed. On l55, near capacity, no policy exceeds 91%.

## Slide 11
RESULTS | GOODPUT
Goodput at high load (24 req/s)
Goodput (%) against deadline, four mixes; 24 req/s is 144%, 107%, 87% and 65% of capacity
Chart: Heavy mix (l55): capacity 16.7 req/s, load 144%
| 150 ms | 600 ms | 2400 ms
Clockwork | 48.2 | 53.5 | 61.7
Greedy-2D | 7.5 | 7.4 | 6
Symphony | 41.3 | 51.9 | 63.9
Chart: Balanced mix: capacity 22.4 req/s, load 107%
| 150 ms | 600 ms | 2400 ms
Clockwork | 63.5 | 74.9 | 83.9
Greedy-2D | 8.7 | 5 | 4.8
Symphony | 54.6 | 68.5 | 83.8
Chart: Skewed mix: capacity 27.5 req/s, load 87%
| 150 ms | 600 ms | 2400 ms
Clockwork | 74.9 | 89.8 | 99.6
Greedy-2D | 8.4 | 2.9 | 16.8
Symphony | 62.5 | 80.4 | 95.3
Chart: Light mix (n70): capacity 36.8 req/s, load 65%
| 150 ms | 600 ms | 2400 ms
Clockwork | 87.1 | 99.5 | 100
Greedy-2D | 50.6 | 97.9 | 100
Symphony | 76.6 | 91.6 | 98.8
Takeaway. Overloaded mixes cap at 84% (balanced) and 62 to 64% (l55), where Symphony matches Clockwork at 2400 ms. On skewed Clockwork keeps 75 to 100% against Symphony 62 to 95%. Greedy-2D is at 3 to 17% on the three heavier mixes.

## Slide 12
RESULTS | GOODPUT
Greedy-2D spirals when load nears capacity
Skewed mix, 24 req/s (87% of capacity), mean of 3 seeds
Policy | Deadline | Goodput | Mean latency | Mean batch size
Greedy-2D | 150 ms | 8.4% | 8.6 s | 1.02
Greedy-2D | 600 ms | 2.9% | 9.1 s | 1.03
Greedy-2D | 2400 ms | 16.8% | 8.6 s | 1.24
Clockwork | 150 ms | 74.9% | 0.08 s | 1.17
Clockwork | 600 ms | 89.8% | 0.35 s | 2.15
Clockwork | 2400 ms | 99.6% | 0.8 s | 3.88
Mechanism
1. The oldest job outlives its deadline, so no batch size fits.
2. The rule falls back to b = 1: service falls below the arrival rate.
3. The queue never drains, because the policy never sheds.
This is my own greedy policy inspired by EdgeServing, without the paper's exit and depth knobs, which shorten service under pressure. It is not a claim that EdgeServing itself fails. In the ladder it spirals above roughly 65 to 85% of a mix's capacity; below that it ties with Clockwork.
Takeaway. A deadline-aware policy that never drops cannot recover from overload. Shedding (Clockwork, Symphony) is what keeps goodput up.

## Slide 13
RESULTS | ENERGY
Total energy at low load (8 req/s)
Total board energy over the same fixed 120 s measured window for every run (idle draw included, no 5 V system rail), against deadline; four mixes
Chart: Heavy mix (l55): capacity 16.7 req/s, load 48%
| 150 ms | 600 ms | 2400 ms
Clockwork | 777 | 913 | 914
Greedy-2D | 931 | 912 | 912
Symphony | 760 | 829 | 739
Chart: Balanced mix: capacity 22.4 req/s, load 36%
| 150 ms | 600 ms | 2400 ms
Clockwork | 688 | 741 | 744
Greedy-2D | 749 | 744 | 745
Symphony | 666 | 687 | 653
Chart: Skewed mix: capacity 27.5 req/s, load 29%
| 150 ms | 600 ms | 2400 ms
Clockwork | 632 | 668 | 666
Greedy-2D | 671 | 667 | 667
Symphony | 611 | 629 | 591
Chart: Light mix (n70): capacity 36.8 req/s, load 22%
| 150 ms | 600 ms | 2400 ms
Clockwork | 554 | 568 | 597
Greedy-2D | 571 | 569 | 570
Symphony | 547 | 551 | 531
Number above each bar: % of requests dropped (cancelled by the policy or lost to queue overflow). Greedy-2D mostly does not drop (queue overflow only at 24 req/s on the two heaviest mixes), but its requests complete late.
Takeaway. Symphony spends the least energy on every mix: at 2400 ms 11 to 19% less than Clockwork, at 150 ms 1 to 3% less, partly because it drops more (6% against 0% at 2400 ms on l55). Greedy-2D matches Clockwork from 600 ms.

## Slide 14
RESULTS | ENERGY
Total energy at medium load (16 req/s)
Total board energy over the same fixed 120 s measured window for every run (idle draw included, no 5 V system rail), against deadline; four mixes
Chart: Heavy mix (l55): capacity 16.7 req/s, load 96%
| 150 ms | 600 ms | 2400 ms
Clockwork | 1001 | 1234 | 1273
Greedy-2D | 1197 | 1195 | 1194
Symphony | 967 | 1167 | 1221
Chart: Balanced mix: capacity 22.4 req/s, load 71%
| 150 ms | 600 ms | 2400 ms
Clockwork | 932 | 1115 | 1129
Greedy-2D | 1165 | 1141 | 1121
Symphony | 884 | 994 | 984
Chart: Skewed mix: capacity 27.5 req/s, load 58%
| 150 ms | 600 ms | 2400 ms
Clockwork | 852 | 982 | 985
Greedy-2D | 1009 | 987 | 987
Symphony | 804 | 890 | 826
Chart: Light mix (n70): capacity 36.8 req/s, load 43%
| 150 ms | 600 ms | 2400 ms
Clockwork | 756 | 807 | 807
Greedy-2D | 811 | 806 | 806
Symphony | 719 | 743 | 714
Number above each bar: % of requests dropped (cancelled by the policy or lost to queue overflow). Greedy-2D mostly does not drop (queue overflow only at 24 req/s on the two heaviest mixes), but its requests complete late.
Takeaway. Symphony is again lowest on every mix (at 2400 ms 4% below Clockwork on l55, 12 to 16% on the others). Greedy-2D sits at the saturation level (about 1.1 to 1.2 kJ) wherever it collapses, because the board runs at full tilt but serves little.

## Slide 15
RESULTS | ENERGY
Total energy at high load (24 req/s)
Total board energy over the same fixed 120 s measured window for every run (idle draw included, no 5 V system rail), against deadline; four mixes
Chart: Heavy mix (l55): capacity 16.7 req/s, load 144%
| 150 ms | 600 ms | 2400 ms
Clockwork | 1101 | 1240 | 1245
Greedy-2D | 1165 | 1160 | 1151
Symphony | 1069 | 1239 | 1252
Chart: Balanced mix: capacity 22.4 req/s, load 107%
| 150 ms | 600 ms | 2400 ms
Clockwork | 1060 | 1216 | 1246
Greedy-2D | 1123 | 1123 | 1121
Symphony | 1006 | 1156 | 1225
Chart: Skewed mix: capacity 27.5 req/s, load 87%
| 150 ms | 600 ms | 2400 ms
Clockwork | 991 | 1177 | 1215
Greedy-2D | 1124 | 1119 | 1137
Symphony | 925 | 1076 | 1110
Chart: Light mix (n70): capacity 36.8 req/s, load 65%
| 150 ms | 600 ms | 2400 ms
Clockwork | 906 | 1016 | 1025
Greedy-2D | 1047 | 1026 | 1023
Symphony | 843 | 915 | 911
Number above each bar: % of requests dropped (cancelled by the policy or lost to queue overflow). Greedy-2D mostly does not drop (queue overflow only at 24 req/s on the two heaviest mixes), but its requests complete late.
Takeaway. Energy rises toward a ceiling of about 1.25 kJ as the board saturates. Symphony stays lowest on skewed (9% below Clockwork at 2400 ms) and the light mix (11%), and level with Clockwork on the overloaded heavy and balanced mixes.

## Slide 16
RESULTS | THE GAP
Goodput against total energy: more goodput costs more energy
Skewed mix, three loads; each point is a policy at one deadline; total board energy over the 120 s window; mean of 3 seeds
Chart: Low load: 8 req/s (29% of capacity)
| 632 | 668 | 666 | 671 | 667 | 667 | 611 | 629 | 591
Clockwork | 93.5 | 100 | 100
Greedy-2D | 91.5 | 100 | 100
Symphony | 82.1 | 91.6 | 97.9
Chart: Medium load: 16 req/s (58%)
| 852 | 982 | 985 | 1009 | 987 | 987 | 804 | 890 | 826
Clockwork | 84.5 | 99.3 | 100
Greedy-2D | 62.8 | 98.9 | 100
Symphony | 70.9 | 87.9 | 97.2
Chart: High load: 24 req/s (87%)
| 991 | 1177 | 1215 | 1124 | 1119 | 1137 | 925 | 1076 | 1110
Clockwork | 74.9 | 89.8 | 99.6
Greedy-2D | 8.4 | 2.9 | 16.8
Symphony | 62.5 | 80.4 | 95.3
Labels mark the deadline for Clockwork and Symphony. Greedy-2D is unlabelled: at 16 and 24 req/s it collapses (3 to 17% goodput at 24 req/s) and still spends about as much energy as the others.
Takeaway. Symphony always spends less than Clockwork, but at 150 ms Clockwork's 3 to 7% extra energy buys 11 to 14 points of goodput, while at 2400 ms its 10 to 19% extra buys only 2 to 4. No policy reaches high goodput at low energy.

## Slide 17
PART 5 | CITYFLOW DISPATCHER
CityFlow dispatcher: methodology
PERTINENCE-style NSGA-II dispatcher search on CityFlow CCTV frames
Step | What was done
Label | A frame is correct for a model if its box recall against yolov8l is at least 0.80 (IoU 0.5, road classes, conf 0.25). Ideal label = cheapest correct model; yolov8l is correct by definition. CityFlow GT has no classes and covers only vehicles seen by 2 or more cameras, so yolov8l is the reference
Model pool | yolov8 n, s, m fine-tuned on CityFlow frames (v1); l stock. Fine-tuning on pseudo-labels from S05
Dispatcher | Frame embedding from a 3.156 GFLOP extractor, then a fully connected head. 13-gene chromosome, population 50, 50 generations, penalty-matrix loss, INS / ISNS / ENS class weighting; 2,500 evaluations, front over all evaluations
Split (clean protocol) | Head trained on S05 camera fold A (7,729 frames); NSGA-II fitness on S05 fold B (7,046 frames); final result reported once on S02
Metric | alpha_sys (fraction of frames routed to a correct model) against GFLOPs, extractor cost included; compared with the static n / s / m / l policies and their hull
Takeaway. Labels, pool and split were fixed before looking at S02, and S02 was scored once.

## Slide 18
PART 5 | CITYFLOW DISPATCHER
CityFlow dispatcher: the fix did not work
S02 result, scored once. Static policies against the NSGA-II front (v1 pool, v1 labels)
Policy | alpha_sys | GFLOPs | Note
Static n | 0.518 | 8.7 | 
Static s | 0.780 | 28.6 | 
Static m | 0.867 | 78.9 | 
Static l | 1.000 | 165.1 | 
Oracle (cheapest correct) | 1.000 | 32.1 | about 80% cheaper than always-l
Dispatcher, clean protocol (S05 folds) | +0.013 over hull | 146 | 109 front points, 8 above the static hull; 84% of frames sent to l
Dispatcher, train-split protocol | +0.038 over hull | 21.8 | 28 of 119 above hull; 50% n / 50% s; train labels 88% n, not trustworthy
No front point is balanced (largest share at most 0.7 and smallest at least 0.05) in either protocol.
Takeaway. The headroom is real (the oracle is far cheaper than always-l), but the dispatchers that came out are at best on par with static policies. I could not build a working dispatcher, so the CityFlow routing fix is not delivered.

## Slide 19
PART 5 | CITYFLOW DISPATCHER
Why it failed, and what is still open
Parked, not closed. The cause is not isolated yet
Finding | Detail
Translating labels for fine-tuning did not help | Relabelling CCTV frames by box recall and fine-tuning on the result did not give dispatchers that route correctly; the dispatchers formed were not correct on the fine-tuned models
Fine-tuning flaw (v1) | The fine-tune ran the bias parameters at a learning rate several hundred times too high in the first two epochs (a library default), so the saved models are weak, especially m
Fix written, not run | The fine-tuning script is corrected (warm-up learning rate), but the retrain and the dispatcher rerun on the new models need the laptop GPU and have not been run
Open causes | Label criterion (per-frame F1 vs confident l boxes, count tolerance, temporal window, a reference beyond l); the weak v1 pool; single-frame features. A label shoot-out on cached data needs no GPU
Earlier signal (week 6) | COCO-trained dispatcher heads collapse on CityFlow: 67 of 93 heads send more than 95% of frames to one model (domain shift)
Takeaway. Decision: parked so the week could go to the Jetson work, since the generic scheduler needs hardware numbers, not routing.

## Slide 20
RESULTS | THE GAP
Limits of these results
What I would not claim yet
Limit | Detail
One board, one backend | AGX Xavier, eager FP16, YOLOv8 only; TensorRT may change the batch-time curve
Few seeds | 2 to 3 per point; on the skewed mix goodput varies by at most 2 points and energy by 2 to 3%
Overload is not steady state | Runs above capacity show spiral and shedding behaviour; Little's law fails there by design
Energy has soft spots | Sampler runs at 8.25 Hz; the busy/idle split is not clean ('idle' gaps draw about 7.4 W against a 2.9 W floor)
Total energy includes idle draw | Energy is the whole board over a fixed 120 s window, idle draw included; a policy that drops requests does less work and spends less, so read it next to goodput
Hypotheses, not results | Symphony's drops on one GPU look like window collisions between queues, and Clockwork might drop the slow queues unfairly; neither is checked yet
Takeaway. The ranking of the policies is consistent across mixes; the exact percentages are not (2 to 3 seeds, one board, eager FP16).

## Slide 21
NEXT
Next steps and questions
Next
Decide on CityFlow: label shoot-out on cached data (no GPU), then v2 fine-tune and dispatcher rerun on the laptop GPU.
Finish seed 2 for the later mixes (about 10 h left) and rerun the analysis.
Calibrate every batch size from 1 to 16 (odd-size slowness).
Fix the sampler cadence (8.25 Hz to 10 Hz).
Check the Symphony collision hypothesis in batches.csv and Clockwork's per-queue fairness.
Define index_T and run it on the same ladder.
TensorRT backend as a realism step.
Questions for the meeting
Is a policy that defers only when slack is large and no other queue needs the GPU the right angle for the paper? (hypothesis: defer and batch like Symphony when there is slack, shed like Clockwork when there is not)
Is goodput under a deadline the right headline, or should the energy-latency Pareto front be primary?
Is eager FP16 acceptable for the evaluation, or should TensorRT come first?